## Slide 1
Inverse Kinematics Model
Given the position and orientation of the end-effecter, determination of joint angles/displacements of a
manipulator is called Inverse Kinematics.
Ex:
For the given 3-DoF articulated manipulator, as shown aside,
the position and orientation of the end-effecter is given as
below. Determine the angles of the three joints to reach the
given position and orientation. Given L1=50; L2=40; L3=20
Picture taken from Robotics and Control by Nagrath and Mittal

## Slide 2
The common procedure is to derive the forward kinematics model and then compare that matrix with the
given matrix term by term and solve for the joint angle.
How to compare:
Position vector elements are to be compared first; such solution is more efficient.
Look for equations involving only one joint variable.
Then look for pairs or sets of equations which can be reduced to one variable.
Arctan is preferable compared to arcsin or arccos
After finding out some angles, if you are not able to proceed further, then we have to think of pre or
post-multiplication. For example, while comparing 0T3 with its counterpart (R), we solved for θ1, not
able to proceed further. Then we should post-multiply 2T3-1 to both sides of the equation (0T3=R). By
that the equation reduces to θ1 and θ2; now θ2 can be determined since θ1 is known. Similarly, if θ3
is known, we should pre-multiply 0T1-1 .

## Slide 3
From forward kinematics, 0T3 is derived as shown below and it is compared to given matrix.
= ……(1)
Determination of θ1
Comparing term(1,4) and (2,4) both sides, we get
C1(L3C23+L2C2)=0…………..(2)
S1(L3C23+L2C2)=-52.779…...(3)
Here, sin is –ve and cos is zero implies it is in the third quadrant and the value is 270o. Here one thing to
note - if we compare term (1,3) or (2,3) we will not get the correct answer. Comparing term (2,3) we
would have got θ1=90o and comparing term (1,3) we would have θ1=-90o.

## Slide 4
We may not get any further individual joint value. But we can get the following.
Comparing term(3,1) and (3,2) both sides, we get
S23=.707…………..(4)
C23=.707……..…...(5)
In the above expression of θ23, since both sin and cos are +ve, the angle lies in the 1st quadrant. So it is 45o.
Since, we cannot proceed further, we have to resort to pre or post multiplication. In this case, since θ1 is already determined, we should post-multiply 2T3-1 to both sides of Eqn. 1.

## Slide 5
………………..(6)

## Slide 6
So Eqn.(6) can be rewritten as follows:
……………(7)
Since, orientation part involves θ3 , it is not required to be determined. Now equating the terms of position vector, we get
L2C1C2=0 ……………(8)
L2S1C2=.707L3-52.779=.707*20-52.779=-38.639 ……………(9)
L2S2=-.707L3+24.49=-.707*20+24.49=10.35 ……………(10)
Squaring and adding Eqn.(8) and (9),
……………….(11)
Here 10.35/38.639=.2679.
---------------------(12)

## Slide 7
So one solution is tan-1(.2679) in the first quadrant and the other is tan-1(-.2679) in the 2nd quadrant because in the 2nd quadrant, sin is +ve and cos –ve. So tan-1(.2679) in first quadrant is 15o. And
tan-1(-.2679) in 2nd quadrant = -15o+180o since tan is periodic with 180o. This is how we should infer from Eqn.(12)
Hence θ3= θ23- θ2=45o-15o or 45o-165o=30o or -120o.
So the solution is θ1=90o; θ2=15o or 165o; θ3=30o or -120o
Sometimes, question may be to derive a generalized inverse kinematics model. In that case, we have equate 0T3 with a general given matrix called [R] where