## Slide 1
Trajectory Planning
Picture taken from Robotics and Control by Nagrath and Mittal
Generation of time sequence of position, velocity and acceleration in terms
of joint or Cartesian coordinates is called trajectory planning. When the time
sequence is in terms of joint coordinates it is called joint space
trajectory planning and when it is in terms of Cartesian
Coordinates it is called Cartesian space trajectory planning.
Path planning vs Trajectory planning: Trajectory planning is with
time history.
Joint Space Trajectory Planning:
Given for a task: Beginning pose, End pose and time required:
Do IK at beginning pose, determine the initial joint angles
Do IK at the end-pose, determine the final joint angles
Interpolate the intermediate joint angles with time history.

## Slide 2
Example:
The base joint of a 3-DOF articulated robot has an initial joint angle of
30o and a final joint angle of 120o for a specific task which takes 10 sec.
Perform Joint space trajectory planning.
t=0 sec t=10 sec
30o 120o If we give these two commands using an Arduino, it will be executed immediately.
We cannot ensure the time duration. How to ensure time duration? Answer is interpolation.
A possible solution
t=0 sec t=1s t=2s t=3s t=4s t=5s t=6s t=7s t=8s t=9s t=10 sec
30o 39o 48o 57o 66o 75o 84o 93o 102o 111o 120o
This is called a linear interpolation. If joint displacement is linear, speed will be constant and zero
acceleration. This is not possible. For quadratic joint displacement, speed will be linear and acceleration is
constant. A preferred interpolation technique is cubic spline trajectory.
Joint space trajectory planning is used for point-to-point tasks. Ex: Pick and place, peg in a hole etc
Cartesian space path planning is used to continuous tasks. Ex: welding, painting etc
Picture taken from Robotics and Control by Nagrath and Mittal

## Slide 3
Cubic Spline Trajectory Planning:
A 1 DOF manipulator with rotary joint is to move from 113o to 210o in 7 sec. Find the coefficients of the
cubic polynomial to interpolate a smooth trajectory. Plot the position, velocity and acceleration variation as
a function of time.
Solution:
q(t)=Co+C1t+c2t2+c3t3 …………………(1)
Given q(0)=113o, q(7)=210o. For a smooth trajectory and .
Application of the constraints:
Applying q(0)=0, we get Co=113;
Applying q(7)=210, we get 210=113+7C1+49C2+343C3 …..............(2)
Applying : ………….(3)
Applying : …………….(4)
Eqn.(2) can be rewritten as ………………(5)
Solving Eqn. 4 and 5, we get C2=5.938 and C3=-.565. So Eqn.(1) is q(t)=113+5.938 t2-.565 t3.

## Slide 4
t
t
t
0 1 2 3 4 5 6 7
0 1 2 3 4 5 6 7
0 1 2 3 4 5 6 7
15
10
5
11.876
-11.876
11.876-3.39t=0
t=3.5
t=3.5
t=3.5
20.802 deg/sec
-x2=4ay
Y2=4ax
x2=4ay
113o
210o
Position
Velocity
Acceleration